G50B

GSM Alarm System

User Manual

2.1 Main unit layout

- Switch to B: Built-in speaker and built-in monitoring effective

- Switch to A: External speakers and built-in monitoring and effective

- Switch to C: Built-in speakers and external monitor effective.

Arm/disarm by SMS

SMS for remote arm: 4 numbers for password +A1

SMS for remote disarm: 4 numbers for password +A2

Example: The host’s password is ……. If you want to set the host in arm mode.

Send SMS: ……A1

Inquire host’s arm/disarm status

Input SMS: 4 numbers for password + W1

Reply SMS: The host’s arm/disarm status

Inquire host’s external power status

Input SMS: 4 numbers for password + W2

Reply SMS: The host’s external power status

Usage

Arm/disarm by remote controller

a) Arm: Press “” on remote controller, the host will make “di” sound, the LCD display is on, “” is twinkling. 30 seconds later, the host enters into arm mode and the “” is on. If you want to arm the system quickly, please press “”.

b) Partial arm: press “”, the host will make “di” sound, the LCD display is on. “” is twinkling. 30 seconds later, the host enters into partial arm mode and “” is on. Press the “”, the host will enter into partial arm mode immediately.

c) Disarm: Press “” to close the system, the host enters into disarm status after the host makes “di, di” sound and the “  ” is on.

Disarm by keyboard on the host

In arming status, press "Disarm" button, when “SET,” appears on the LCD display, then Input: password + OK will disarm

Note: Keypad will become invalid when in alarm state.

Auto detect doors and windows closed properly

It will sound when delay arm or partial arm in a state of alarm from wired zone. LCD will show 1 or 2, means wired zone 1 or wired zone 2 cable input are not normal. (This can be used for the wired windows/doors Magnetic Contact to check doors/windows close properly before go out)

Emergency alarm

When an emergency alarm occurs, press “” and the host will enter into emergency alarm status immediately and the siren will alarm for 90 seconds to inform the neighbors. At the same time, it will automatically dial the preset alarm phone numbers cycled for three times and send SMS of “Emergency alarm”

External power failure alarm

When the system checks out that there is something wrong with the external power or the external power is off for more than 2 seconds, it will enter into alarm status immediately. At the same time, the system will automatically dial the preset phone numbers cycled for three times and send the SMS of “External power failed”.

When the power supply is on, the system will stop alarming immediately and send the SMS of “External power is OK”.

LCD alarm instructions

When alarming, the screen display”, SMS, TEL" and alarm zone number (“OP" means power failure, "OE" means emergency call, "OF" means fire, 01-26 are wireless alarm zones, 55 for the tamper alarm), warning for 90 seconds.

Alarm and Handle

The siren sounds loudly for 90 seconds to inform the neighbors. At the same time, the system automatically sends SMS alert and auto-dial the 3 group preset phone numbers in 3 turns. The user can listen to the pre-recording warming voice and enter monitoring status which supports two ways communication.

If the user answers the alarm call, the host will stop dialing the next preset alarm number, then press any phone button can off the siren.

Or else, the system will auto-dial the next phone number if the phone can’t put through such as the line is engaged or drop call.

Operation Cautions

- Check all the detectors and their battery in time and change them when voltage is low.

- This product is designed for the indoor use rather than outdoor use.

# Text boxes

Wired zone connector

Recording status indicator & Record button

Power connector of the host

Wireless signal-receiving indicator

Tamper switch

Power switch